## Slide 1: On-Chip Communication Architectures
Models for Power and
Thermal Estimation
ICS 295
Sudeep Pasricha and Nikil Dutt
Slides based on book chapter 5
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 2: Outline
Introduction
Models for Power Estimation of Wires
Models for Power Estimation of On-Chip Communication Architectures
Models for Thermal Estimation
PVT variation-aware Power Estimation
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 3: Introduction
Power today is an important multi-processor system-on-chip (MPSoC) design constraint
  for mobile applications such as cellular phones, MP3 players, and laptops with fixed battery budgets
    e.g., watching several movies on a single battery charge is virtually impossible on today’s devices
  for non-portable applications server farms
    e.g., as much as 2 megawatts for a 25,000 square foot server farm with 8000 servers
In future silicon technologies increasing operating frequencies and transistor densities will make power dissipation a major concern
Note: Power, Energy used interchangeably from here onwards
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 4: Introduction
Power dissipation has an undesirable thermal side effect of increasing device temperature -> affects reliability of MPSoCs
  Reliability: probability that system will operate correctly at any given time of operation
    measured by mean time to failure (MTTF)
Need to extend MTTF beyond expected life of a product
  for critical systems used in aircraft control, automotive control, medical equipment, defense applications
Temperature cycles/spikes due to excessive power dissipation cause:
  Specific failure in components/wires
  Secondary effects such as timing failure and data corruption
Techniques to estimate and reduce power consumption are essential for lowering operating temperatures
  so that the MTTF is increased and cooling /packaging costs reduced
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 5: Introduction
On-chip communication architectures have a considerable impact on MPSoC power dissipation in DSM technologies
  coupling/parasitic capacitance increasingly dominant
  interconnect capacitance a large portion of chip capacitance
  large number of repeaters and vias to reduce wire delay in DSM technologies doubles power dissipation in interconnects
  state of the art communication architectures also have significant amounts of hardware logic
    e.g., bridges, arbiters, decoders, buffers, etc.
    comparable to logic in embedded processors of moderate complexity
Need to create models for estimating power consumption of on-chip comm. architectures early in a design flow for MPSoCs
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 6: Introduction
Power and thermal estimation models in a typical electronic system level (ESL) design flow
Need to be close to implementation to get accurate power and thermal information
Challenge: extrapolating information from lower levels in the design flow up to the system level
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 7: Outline
Introduction
Models for Power Estimation of Wires
Models for Power Estimation of On-Chip Communication Architectures
Models for Thermal Estimation
PVT variation-aware Power Estimation
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 8: Bus Wire Power Models
Power consumption in CMOS logic gates can be expressed by the following general equation:
Like logic gates, wires have a capacitance as well
  represents charge to be added/removed to change electrical potential
  whenever a data bit is transmitted on a bus wire, the charging and discharging of this wire capacitance results in power consumption
Accurate modeling of wire capacitance is a non-trivial task
  structure of a wire in contemporary integrated circuits (ICs) is 3-D
  capacitance of such a wire is a complex function of its shape, environment, distance to substrate, distance to surrounding wires, etc.
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 9: Bus Wire Power Models
Early work expressed bus wire power consumption as
where ntrans is
Hamming distance for a 16 bit wide bus:
  word on the bus at time t is 1000100011001100
  word on the bus at time t +1 is 1001100110001000
then is the number of bit-flips = 4
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 10: Bus Wire Power Models
Chern et al. [EDL ‘92] proposed a model for wire capacitance
  three primary constituents of wire capacitance
    line-to-line capacitance
    line-to-ground capacitance
    crossover capacitance
  For wire on metal layer 2,
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 11: Bus Wire Power Models
In the model, complex capacitance expressions were derived
  e.g., line-to-ground capacitance was calculated as:
where
W is the metal width
S is the space between two lines (or wires),
T is the thickness of the metal,
H is the thickness of dielectric layer between metal layers
ɛ is the dielectric constant
Measurements indicated an accuracy of within 8% for capacitance values
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 12: Bus Wire Power Models
More accurate analytical models (Ho et al. [IEEE 2001]) combine a bottom plate term with a fringing term
  to account for field lines originating from edge and top of wire
Capacitance can then be modeled by four parallel plate capacitors for the top, bottom, left, and right sides, plus a constant term for fringing capacitance
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 13: Bus Wire Power Models
Vertical and horizontal capacitors can have different relative dielectrics for technologies that use low K materials, and the wire capacitance is expressed as
Capacitances to the left and right have data dependent effective capacitances
  if left and right neighbors of a wire switch
    in opposite direction as the wire, then the effective side capacitances double
    with the wire, the effective side capacitance approaches zero
  this effect is termed as Miller multiplication and is modeled by varying the K parameter between 0 and 2 in the equation
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 14: Coupling-Aware Wire Power Models
Significant amount of work has modeled the capacitive (and inductive) parasitic interactions and coupling of bus wires in DSM technologies
Sotiriadis et al. [TVLSI 2002] proposed an equivalent capacitive network model for the DSM bus
  lumped energy equivalent DSM bus model
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 15: Coupling-Aware Wire Power Models
The energy drawn during a transition, from the power supply by the bus drivers, for a bus with n lines is
where
, are vectors with n coordinates representing initial and final voltages on bus lines
ei is a vector with a 1 in the ith position, and 0 elsewhere
Ct is the total capacitance conductance matrix
  which represents the capacitances between the lines and ground
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 16: Coupling-Aware Wire Power Models
Proposed model was simplified to ignore parasitics between non-adjacent lines
Approximate total capacitance conductance matrix:
Parameters λ and ζ depend on CMOS technology used, as well as specific geometry, metal layer, and shielding of the bus
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 17: Coupling-Aware Wire Power Models
Kretzschmar et al. [DATE ‘04] proposed an analytical model for power dissipation on a bus, accounting for repeaters
Wire capacitance per unit length is
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 18: Coupling-Aware Wire Power Models
Average capacitance of bus is given by:
where L is the length of the line and d is the inter-repeater distance.
Bus power can be obtained by plugging capacitance into the following equations:
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 19: Coupling-Aware Wire Power Models
Gupta et al. [ICCAD 2003] proposed a bus power model for use in high level exploration
Switching power PSW uses a table lookup technique
  low level transistor simulation used to construct a three-wire lookup table for minimally spaced wires of various lengths
  gives power consumption for each type of transition in the transition set
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 20: Coupling-Aware Wire Power Models
Power of vias Pvias
number of vias VN estimated using interconnect layout with floorplanner and statistical methods, and then counting number of times an interconnect changes direction
via power Pvia dependent on the layer in which it resides
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 21: Coupling-Aware Wire Power Models
Power due to repeaters Prepeaters
ρi is the switching activity
number of repeaters NR are obtained from formulations presented by Kapur et al. [6] and Bakoglu et al. [45]
  which give optimal inter-repeater distance for given CMOS technology
total number of repeater vias VR are calculated to be twice the number of repeaters
  since paths are needed to descend and ascend from substrate where repeaters reside
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 22: Outline
Introduction
Models for Power Estimation of Wires
Models for Power Estimation of On-Chip Communication Architectures
Models for Thermal Estimation
PVT variation-aware Power Estimation
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 23: Power Estimation of On-Chip Communication Architectures
In addition to wires, an important component of on-chip communication architectures is bus logic
Bridges, arbiters, decoders, buffer stages, etc. have a significant contribution towards on-chip power
Important to account for power contribution for both bus logic and bus wires
Especially true for increasingly complex communication architectures being used in multi-core SoC designs today
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 24: Power Estimation of On-Chip Communication Architectures
Lahiri et al. [CODES+ISSS 2004] proposed gate level power estimation methodology for estimation of logic and bus wire power for AMBA AHB/APB
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 25: Power Estimation of On-Chip Communication Architectures
Methodology was used to obtain breakdown of power consumed by various components of the AMBA bus
Bus lines (wires) consume only 14% of overall power
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 26: Power Estimation of On-Chip Communication Architectures
Pasricha et al. [CODES+ISSS 2006] proposed an energy macro-model based methodology to estimate power for bus matrix communication architectures at the system-level
An energy macro-model for a component has two basic elements
  variables – that represent factors (events) influencing energy consumption
    Control (e.g. signal value changes)
    Data (e.g. Hamming distance of input data values)
    Structural (e.g. bus widths)
  regression coefficients – that capture correlation between the variables and energy consumption
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
Linear model

## Slide 27: Power Estimation of On-Chip Communication Architectures
Created energy macro-models for all bus matrix logic components
  Input Stage
  Decoder
  Output Stage
  Arbiter
Energy consumption of wires at system-level, is given as
  Simulated annealing floorplanner for IP placement and wire length estimation
    Adya et al. [TVLSI 2003]
  Berkeley Predictive Technology Model (PTM) for ground, coupling capacitance
  Repeater capacitance, leakage power from data sheets
  Optimal-delay repeater sizing/spacing
EINP = αinp0 + αinp1.Ψload + αinp2.Ψdesel + αinp3.ΨHDin + αinp4.Ψdrive

## Slide 28: Power Estimation of On-Chip Communication Architectures
Methodology overview
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 29: Power Estimation of On-Chip Communication Architectures
Macro model template for input buffer component of bus matrix
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 30: Power Estimation of On-Chip Communication Architectures
Macro model coefficients for bus matrix (180 nm)
R2 value close to 1 (implies reliable prediction with model)
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 31: Power Estimation of On-Chip Communication Architectures
Regression coefficients for input stage component
  across various CMOS technology nodes (180 – 65 nm)
Easy to retarget methodology to different technology nodes
  generate gate level cycle energy numbers with new library for small system testbenches
  use these to update cycle energy column in the macro-model template
  repeat regression analysis (~ few minutes)
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 32: Power Estimation of On-Chip Communication Architectures
Compared accuracy of energy macro-model estimates with gate-level estimates using Synopsys PrimePower
Highly accurate cycle energy estimation that is unaffected by the scaling of technology libraries
Maximum average cycle energy estimation error only 4.19%
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 33: Power Estimation of On-Chip Communication Architectures
Plugged macro-models into TLM-based bus-cycle accurate (T-BCA) simulation environment in SystemC and compared power waveform accuracy with gate-level estimation
Highly correlated waveforms – useful for peak power estimation
  assist planning of power grids
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 34: Power Estimation of On-Chip Communication Architectures
Compared CPU time taken for the PrimePower simulation (for gate level cycle energy estimation) with the system level CCATB-based prediction
Significant ~ 2000x speedup possible using system level power estimation
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 35: Power Estimation of On-Chip Communication Architectures
Caldari et al. [DATE 2003] proposed energy macro models for an AMBA AHB bus
Models created for arbiter, decoder, multiplexing logic
  For e.g., decoder macro model
where n0 ≥ 2 is number of slaves attached to decoder
n1 is first integer number greater than log2(n0-1)
CO is capacitance of each output node
CPD is equivalent capacitance of one node
HDOUT is 1 if HDIN ≥ 1
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 36: Power Estimation of On-Chip Communication Architectures
Models were used to create a higher level instruction model for AHB power consumption
Four main activity modes were identified on the bus: IDLE, READ, WRITE, and IDLE with bus handover
Drawbacks: did not consider static/leakage power, or power due to bus wires
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 37: Power Estimation of On-Chip Communication Architectures
Bona et al. [DATE 2004] proposed macro-models to estimate power consumption for the crossbar (or shared bus) topology-based Type 2 and Type 3 STBus
Macro-model represents an STBus configuration n in design space S:
where i is the number of initiators (or masters)
t is the number of targets (or slaves)
rqr, rpr are the no. of request or response resources, p is the type of arbitration policy,
CL is the total output pin capacitance
dps is the data path width (e.g., 32 or 64 bits)
Type is the protocol mode (either Type 2 or Type 3)
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 38: Power Estimation of On-Chip Communication Architectures
Power dissipation of an STBus configuration n
where B(n), Psent(n), and Prec(n) are linear regression coefficients
B(n) is average base cost of configuration n of node
Psent(n) is additive power of data cells sent from masters
Prec(n) is power cost due to data received by the masters
rS is the total number of data cells sent to the slaves
rr is the total number of data cells received by the masters
C is the total number of clock cycles
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 39: Power Estimation of On-Chip Communication Architectures
Model accuracy explored for power estimation of four ARM7TDMI processor initiators and several targets simulated in SystemC (200K cycles)
System level estimation has an average total error of 9%
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 40: Outline
Introduction
Models for Power Estimation of Wires
Models for Power Estimation of On-Chip Communication Architectures
Models for Thermal Estimation
PVT variation-aware Power Estimation
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 41: Models for Thermal Estimation
Thermal effects are an inseparable aspect of signal propagation
  Current flowing through an interconnect causes power dissipation
Substrate, which is attached to the heat-sink, is typically far away from the interconnect lines (especially global-tier ones)
  heat generated by interconnect cannot be efficiently removed
  leads to increase in interconnect temperature -> Joule heating
With aggressive CMOS scaling, low K inter-layer and inter-metal dielectrics (IMDs) have been introduced
  to reduce RC delay, crosstalk, dynamic power consumption over SiO2
  but low K dielectrics increase interconnect temperature
    have poor thermal conductivities
Increasing no. of metal layers (~6 in 180nm to10 in 50nm) further exacerbates problem of high interconnect temperatures
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 42: Models for Thermal Estimation
Thermal effects have a significant impact on the performance, power, design, and reliability of interconnects because:
  interconnect lifetime (or reliability) has an exponential dependence on the inverse metal temperature
  thermal effects put a limit on maximum allowed root mean square (RMS) current density through the interconnects
  interconnect metal resistivity is dependent on temperature
    e.g., resistivity of Cu increases by 39% from 20°C to 120°C
    higher resistivity causes larger RC delay that degrades performance
  leakage power has a significant dependence on temperature, and can be order of magnitudes greater at high temperatures
  thermally induced open circuit metal failure under short duration high peak currents including electrostatic discharge (ESD) can introduce latent electromagnetic (EM) damage
    ESD is the single largest cause of failures in ICs
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 43: Models for Thermal Estimation
Sotiriadis et al. [TVLSI 2002] proposed a model for the energy dissipated as heat on bus lines
Energy drawn from the power supply consists of two parts:
  energy stored in the capacitances of the repeaters and bus
  energy dissipated as heat
Energy drawn by the ith driver on a bus, which is converted into heat during a transition, is given by
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
Total energy drawn from power supply
Difference in energy stored in capacitances before and after switching

## Slide 44: Models for Thermal Estimation
Eheat0 represents heat generated when bus line is charged
Heat is also generated when a bus line is discharged
Energy converted into heat during bus line discharging is:
Total energy dissipated as heat on driver and bus lines is
E = Eheat0 + Eheat1
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
Difference in energy stored in capacitances before and after transition

## Slide 45: Models for Thermal Estimation
Sundaresan et al. [VLSID 2005] proposed another thermal model for bus lines
Created equivalent electrical and thermal RC network for a 5 bit bus
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 46: Models for Thermal Estimation
Thermal capacitance
Thermal resistance
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 47: Outline
Introduction
Models for Power Estimation of Wires
Models for Power Estimation of On-Chip Communication Architectures
Models for Thermal Estimation
PVT variation-aware Power Estimation
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 48: PVT Variation-aware Power Estimation
In sub 100nm DSM technologies, Process, Voltage and Temperature (PVT) variability is being observed, due to
  Increasing leakage power
  Use of power-aware design methodologies (voltage islands, DVS/DFS)
PVT variability making it hard to achieve safe designs
Results in significant fluctuations in power (and timing)
Power (and timing) estimates from early in the design flow no longer valid
Considerable effort required later in design flow to account for variability-induced fluctuations
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 49: PVT Variation-aware Power Estimation
Traditional (current) power-aware design methodology
Without taking PVT variations into account, early power exploration results can lead to erroneous assumptions
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
System level
RT level
Gate level
A
B
power
power
more time, cost, designer effort
A`
B`

## Slide 50: PVT Variation-aware Power Estimation
Pasricha et al. [VLSID 2008] presented several experimental results to motivate PVT variation aware power estimation at the system-level
Proposed system level PVT corner analysis for more accurate power characterization of comm. architectures
  PVT corners are library characterizations at design corners used by a foundry to communicate PVT variations to designers
  relate cell metrics (timing, power) to PVT variations
Up until 130nm design tools relied on three corners:
  Typical, Worst, and Best corners; +/- 20% variation among corners
  negligible leakage; Vdd major factor influencing power dissipation
For sub-100nm UDSM, many more corners required
  essential to analyze design across these corners
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 51: PVT Variation-aware Power Estimation
Impact of PVT variation on power dissipation of AMBA AHB bus matrix at 90nm
Significant (as much as 10×) variation in power dissipation across PVT corners for on-chip comm. architectures
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 52: PVT Variation-aware Power Estimation
Impact of PVT variation on power dissipation of AMBA AHB bus matrix at 65nm
Significant (as much as 10×) variation in power dissipation across PVT corners for on-chip comm. architectures
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 53: PVT Variation-aware Power Estimation
Proposed PVT-aware power exploration design methodology
PVT variation-aware early power exploration improves design reliability and reduces design time, cost and effort
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
System level
RT level
Gate level
A
B
power
power
less time, cost, designer effort
A`
B`

## Slide 54: PVT Variation-aware Power Estimation
From experimental results, it was determined that
  power consumption for a PVT corner scales almost linearly with freq
  power consumption numbers obtained for different PVT corners show an almost constant ratio relative to each other
Let power consumption of bus matrix comm. architecture for an implementation with PVT corner C1 be:
PC1 = PL1 + PD1 × freq ; PL1 – leakage power PD1 – dynamic power
Then power consumption for an implementation under any other PVT corner C2 can be expressed as:
PC2 = α1-2 × PL1 + β1-2 × PD1 × freq ; α1-2 , β1-2 are scaling relations
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 55: PVT Variation-aware Power Estimation
Values of scaling factors α1-2 , β1-2 found by decomposing total power into leakage and dynamic for PVT corners
  as shown for 65 nm bus matrix case
Less than 5% error for dynamic power and less than 10% error for leakage power in most cases
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 56: Summary
Power is increasingly becoming a first class design objective
  thermal effects of power essential to consider in today’s designs
Contribution of on-chip communication architectures to the overall chip power is rapidly increasing as technology scales
  critical need for accurate estimation models
Presented an overview of several approaches to model
  power consumption of bus wires,
  power consumption of bus logic components
  thermal effects of signal propagation on interconnects
  PVT variations
All of these models are most useful when incorporated into larger frameworks used for communication architecture design/synthesis in an ESL flow
© 2008 Sudeep Pasricha & Nikil Dutt
<number>

## Slide 57
<number>
© 2008 Sudeep Pasricha & Nikil Dutt