## Slide 1: On-Chip Communication Architectures
Models for Performance
Exploration
ICS 295
Sudeep Pasricha and Nikil Dutt
Slides based on book chapter 4
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 2: Outline
Introduction
Static Performance Estimation Models
  Analytical/Estimation-based
Dynamic Performance Estimation Models
  Simulation-based
Hybrid Performance Estimation Models
  Static/dynamic-based
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 3: Introduction
On-chip communication architectures have numerous sources of delay
  signal propagation
  synchronization (e.g., handshaking)
  transfer modes
    pipeline access, burst transfer, etc.
  arbitration mechanisms
  cross-bridge or cross-clock domain transfers
  data packing/unpacking at interfaces
These significantly influence SoC performance and are a major bottleneck in many designs
  important to consider these during SoC exploration
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 4: Communication Architecture Performance Estimation in ESL Design Flow
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 5: Static Communication Architecture Performance Estimation
Attempts to determine the performance of a system through analysis
  closed form expressions that capture system performance as a function of parameters
Key challenge: determine the right set of system parameters and their interactions
Next few slides
  Review of static performance estimation methods
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 6: Static Communication Architecture Performance Estimation
Knudsen et al [CODES 1998] presented a high level estimation model for communication throughput for a given protocol
Delays are estimated for the following components
  Transmitting drivers
  Receiving drivers
  Channel
Approach assumes pipelined transfers and estimates
  burst time,
  data packet splitting/joining time at interface
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 7: Static Communication Architecture Performance Estimation
<number>
transmission delay
channel delay
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 8: Static Communication Architecture Performance Estimation
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
receiver delay
maximum total delay (assuming pipelined operation)
total transmission delay

## Slide 9
<number>
Renner et al [RSP 1999] presented more detailed communication performance estimation models
  transmitter, channel, and receiver delays
  also considers software, wire delay, protocol latencies
Static Communication Architecture Performance Estimation
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 10
<number>
Transmitter/Receiver delay model
n – number of cycles to put data on channel
f – frequency of core
Example timing results of transmitter/receiver part
Static Communication Architecture Performance Estimation

## Slide 11
<number>
Static Communication Architecture Performance Estimation
Channel delay model
Delay for one bit link
Example timing results of channel part
tWIRE = wire delay tSW = switch delay
tFPGA = FPGA delay tDPR = memory access time
where

## Slide 12
<number>
Static Communication Architecture Performance Estimation
Protocol delay model

## Slide 13
<number>
Static Communication Architecture Performance Estimation
Total communication delay
  for a single transmission
  for pipelined transmission

## Slide 14: Static Communication Architecture Performance Estimation
Cho et al. [SLIP 2006] proposed analytical performance model for AMBA 2.0 AHB single shared bus and hierarchical shared bus architectures
Latency of shared bus
    Nd= number of data items to be transferred
    Nm = number of masters on the bus
    B = fixed burst size
    S = probability of single mode transfers on shared bus
    U = usage of the bus, and is a probability of continuing single transfers, in a pipelined manner (helping to reduce Ls)
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 15: Static Communication Architecture Performance Estimation
Latency of hierarchical shared bus
    Nl = number of layers (or buses) in hierarchical shared bus architecture
    A = probability of the path of the data transfer passing through a bridge
    𝛼 = bridge factor; represents latency overhead caused by using bridge
Assumptions of model:
  slave does not introduce any wait states
  request and address phases occur in the same cycle
Using appropriate A, S and U values, an accuracy of 96% and 85% was obtained compared to a simulation-based approach for shared bus and hierarchical bus
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
1

## Slide 16: Limitations of Static Performance Estimation Methods
Require several assumptions that depend on application functionality and are not so easy to model
  e.g., probabilistic values for parameters, single cycle arbitration for all transfers, etc.
Unable to account for non-deterministic traffic generation by the components on the buses
  cannot predict dynamic component (e.g., memory access) delays
Cannot easily account for other sources of dynamic delays, due to
  complex arbitration and traffic congestion, cache misses, burst interruptions, interface buffer overflows, the effects of advanced bus architecture features such as SPLIT/OO transaction completion, etc
Limited applicability for most medium- to large-scale SoCs
  useful for obtaining worst case performance bounds
  can provide (conservative) performance estimates early in design flow
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 17: Dynamic (Simulation-based) Communication Architecture Performance Estimation
Simulate application; capture application specific effects
Several modeling abstractions used by designers
  trade-off simulation speed, modeling effort and accuracy
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 18: Cycle Accurate (CA) Models
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
TLM
PA-BCA
CA
Algorithm
Detailed system debug and analysis
Time consuming to model
  - /1 to /3 RTL
Too slow for exploring SoC designs
  - 100x RTL
var1 = a + b;
wait();
REG = d<<var1;
wait();
HREQ.set(1);
e = REG4 | 0xff
wait();
bus
arb
case CTR_WR:
CTR_WR = in;
wait();
CTR_WR |=0xf;
wait();
ST_RG = in|0x1
wait();
master
slave
pin interface
T-BCA

## Slide 19: Cycle Accurate (CA) Models
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
Loghi et al [DATE 2004] used CA models written in SystemC to explore AMBA2 and STBus communication architectures for MPSoCs

## Slide 20: Pin Accurate Bus Cycle Accurate (PA-BCA) Models
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
High level system exploration
Still time consuming to model
  - /5 to /10 RTL
Still slow for exploring SoC designs
  - 100x to 500x RTL
…
var1 = a + b;
REG = d<<var1;
HREQ.set(1);
e = REG4 | 0xff
wait(3, SC_NS);
…
bus
arb
…
case CTR_WR:
CTR_WR = in;
CTR_WR |=0xf;
ST_RG = in|0x1
wait(3,SC_NS);
…
slave
master
pin interface
TLM
PA-BCA
CA
T-BCA
Algorithm

## Slide 21: Pin Accurate Bus Cycle Accurate (PA-BCA) Models
Séméria et al. [ASPDAC 2000] used PA-BCA models (also called bus functional models or BFM) to improve simulation speed over CA models
  for the purpose of HW/SW co-verification
  modeled in SystemC
  20x speedup if processor ISS model granularity raised
Kalla et al. [ASPDAC 2005] executed traces of component behavior on a PA-BCA simulator
  as much as a 94% speedup over CA simulation model
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 22: Transaction-based Bus Cycle Accurate (T-BCA) Models
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
Uses Transaction Level Modeling (TLM) techniques to speed up BCA model simulation
Time to model varies
Simulation speed generally faster than PA-BCA
…
var1 = a + b;
d = d << var1;
request(port1);
e = REG4 | 0xff
wait(3, SC_NS);
HSEL.set(1);
…
case CTR_WR:
CTR_WR = in;
CTR_WR |=0xf;
ST_RG = in|0x1
wait(3, SC_NS);
…
slave
master
pin, transaction interface
bus
arb
TLM
PA-BCA
CA
T-BCA
Algorithm

## Slide 23: Transaction-based Bus Cycle Accurate (T-BCA) Models
Caldari et al. [DATE 2003] modeled AMBA2 AHB, APB using function calls for reads/writes
  used SystemC 2.0, with clocked threads to capture components
  in addition to read( ) and write( ) transaction functions signals such as HREADY and HRESP were also captured
    to maintain cycle accuracy
  compared PA-BCA model of the STBus and a T-BCA model of the AMBA AHB and APB buses
    showed a speedup of between 3x and 7x for the T-BCA model
    for different traffic profiles on a small SoC testbench
  100x speedup for T-BCA model over a CA model of AMBA AHB
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 24: Transaction-based Bus Cycle Accurate (T-BCA) Models
Ogawa et al. [DATE 2004] created another T-BCA model variant for the AMBA AHB bus architecture
  using C as the modeling language
  explicit low level handshaking semantics with request, response signaling captured
  speedup of about 30x compared to CA model during design space exploration of an AMBA AHB based graphics display SoC
Kim et al. [30] used another approach for T-BCA modeling
  capture signals as function calls, which enables simulation speedup while still maintaining bus cycle accuracy
  used in the Synopsys Cycle Accurate SystemC models for AMBA AHB and APB
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 25: Transaction-based Bus Cycle Accurate (T-BCA) Models
Pasricha et al. [DAC 2004] proposed the Cycle Count Accurate at Transaction Boundaries (CCATB) modeling abstraction
can be modeled in SystemC, or any other modeling language (C, C++, Java, etc)
raises modeling abstraction above T-BCA
maintains overall cycle accuracy, essential for system exploration
uses concepts of transactions from TLM
  no pins modeled
  extension of TLM read(), write() interface
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 26: Transaction-based Bus Cycle Accurate (T-BCA) Models
CCATB read and write (SystemC 2.0)
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 27: Transaction-based Bus Cycle Accurate (T-BCA) Models
Control token structure in CCATB
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 28: Transaction-based Bus Cycle Accurate (T-BCA) Models
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
CCATB model captures all delays encountered by transaction
  clusters timing delays & minimizes no. of actively simulating IPs
  maximizes opportunity to increment simulation time in bursts
Target delay
Interface delay
Communication protocol delay
Arbitration delay
Initiator delay
ITC
interface
TIMER
interface
MEM1
interface
ARM
Processor
interface
MASTER 1
interface
MEM
CONTROLLER
interface
ARBITER
MEM2
MEM3
DMA
interface
AMBA 2.0 Bus

## Slide 29: Contrasting CCATB with Detailed Pin Accurate Abstraction
<number>
CCATB model takes the same amount of time to complete a read/write transaction as a detailed pin-accurate model
CCATB trades off intra-transaction visibility for simulation speed

## Slide 30: Comparing CCATB with Other Abstractions
<number>
Switch
AHB System bus 1
ARM926EJ-S
ROM
SDRAM I/F
Arbiter
DMA
RAM
AHB/APB
Bridge
APB peripheral bus
ITC
Timer
UART
EMC
USB
AHB/AHB
Bridge
AHB System bus 2
RAM
Traffic gen1
Arbiter
AHB System bus 3
RAM
Traffic gen2
Arbiter
Traffic gen3
Compared CCATB performance with PA-BCA and T-BCA models
Explore effect of changing system complexity on simulation speed
  start with simple SoC system
  iteratively add components to increase complexity
  measure simulation speed at each iteration

## Slide 31
<number>
Model Abstraction | Average CCATB speedup (x times) | Modeling Effort
CCATB | 1 | ~3 days
T-BCA | 1.67 | ~4 days
PA-BCA | 2.2 | ~1.5 wks
CCATB takes less time to model than other abstractions
CCATB consistently faster than PA-BCA and T-BCA
Comparing CCATB with Other Abstractions

## Slide 32: Transaction Level Models
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
High level system validation and embedded software development
Fast to model
  - /10 to /50 RTL
Fast simulation speed, but model not too detailed for exploring SoC designs
  - >>1000x RTL
…
var1 = a + b;
d = d << var1;
request(port1);
e = REG4 | 0xff
wait();
…
bus
arb
…
case CTR_WR:
CTR_WR = in;
CTR_WR |=0xf;
ST_RG = in|0x1
wait();
…
slave
master
generic channel interface
channel
TLM
PA-BCA
CA
T-BCA
Algorithm

## Slide 33: Transaction Level Models
TLM can be thought of as a P2P, zero-time interconnection between system components
To enable comm. architecture exploration at the TLM level, some approaches incorporate bus protocol structural and timing details in TLM
  not guaranteed to be very accurate in estimating performance
Arbitrated-TLM (ATLM) add support for arbitration and shared buses, to capture contention during communication
  Pasricha et al. [SNUG 2002]
  Ariyamparambath et al. [ISSOC 2003]
  Schirner et al. [DATE 2006]
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 34: Transaction Level Models
Ariyamparambath et al. [ISSOC 2003] annotated ATLM models with bus-protocol-specific timing details
  Introduced the near cycle accurate (NCA) bus that has timing annotation to capture bus protocol specific delays
  NCA abstract bus model automatically calculates the time delay associated with the data transfer
  Waits for that time delay before calling the slave interface and writing the data to it
  Delay information captures
    Internal bus delay cycles (e.g, request, grant, etc)
    Pipeline delay cycles
    Burst length cycles
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 35: Transaction Level Models
Viaud et al. [DATE 2006] proposed TLM/T (transaction level model with time) abstraction level
  each component modeled as a thread, and has a local clock
  communication via packets transferred on P2P channels
  effect of arbitration modeled by global interconnect model, which includes all the P2P links interconnecting components
  local clocks of two threads are synchronized every time a packet is sent from one thread to the other.
  simulation speed is improved because each (master) component has a local clock, with no need for global synchronization at every system cycle
  Experimental results on a generic OCP/VCI comm. architecture showed a speedup of 10x to 60x compared to a PA-BCA model, at a slight loss in accuracy of less than 1%
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 36: Transaction Level Models
Schirner et al. [CODES+ISSS 2006] proposed result oriented modeling (ROM)
  model initially predicts time taken to complete a transaction, and corrects prediction if required at the end of prediction period
  correction accounts for disturbing influences such as transactions from higher priority masters that can lengthen transaction completion time
  due to the correction mechanism, the model complexity is higher than CCATB and other T-BCA models
  can provide speedup for statically scheduled, predictable applications such as real-time CAN-based systems
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 37: Multiple Abstraction Modeling Flows
Modeling abstractions described till now have had different strengths and weaknesses stemming from inherent trade-off between
  complexity of details captured
  estimation accuracy
  simulation speed
Useful to have a communication-centric exploration flow that integrates several abstraction levels
  allow performance exploration with different levels of captured details, accuracy, and simulation speed in an SoC design flow
A few pieces of work have proposed such communication-centric design space exploration flows
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 38: Multiple Abstraction Modeling Flows
Rowson et al. [DAC 1997] illustrated the use of multiple abstraction levels for communication architecture exploration of an ATM packet network
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 39: Multiple Abstraction Modeling Flows
Hines et al. [DAC 1997] proposed using multiple levels of abstraction for comm. architecture exploration, with the ability to dynamically switch between them
  for greater exploration flexibility in terms of simulation speed and accuracy
  approach allows a designer to switch from a detailed PA-BCA model to less detailed TLM-like models to speed up exploration
Beltrame et al. [DATE 2006] proposed a similar approach
  dynamic switching between BCA, untimed TLM, timed TLM
  to improve simulation speed for exploration
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 40: Multiple Abstraction Modeling Flows
Haverinen et al. [OCP White Paper 2003] proposed a stack of comm. abstraction layers, each having a different level of detail for modeling comm. in a design flow
  adapted for use in the LISA Processor Design Platform, to jointly design and explore processor architecture with an on-chip communication architecture
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 41: Multiple Abstraction Modeling Flows
Kogel et al. [CODES+ISSS 2003] made use of 3 of the abstraction levels from the comm. layer stack to explore design of a network processing unit for IP forwarding
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 42: Multiple Abstraction Modeling Flows
Pasricha et al. [DAC 2004] proposed another variant of communication-centric design flow
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 43: Hybrid Performance Estimation Approaches
Hybrid performance estimation techniques
  combine static and dynamic performance estimation strategies
  speed up comm. architecture performance estimation while generating accurate performance exploration results
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 44: Hybrid Performance Estimation Approaches
Lahiri et al. [VLSID 2000] proposed a hybrid trace-based comm. architecture performance exploration technique
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
dynamic
static

## Slide 45: Hybrid Performance Estimation Approaches
Trace generated from simulation phase
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 46: Hybrid Performance Estimation Approaches
CAG generated from simulation trace
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 47: Hybrid Performance Estimation Approaches
Augmenting CAG with comm. protocol details in static phase
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 48: Hybrid Performance Estimation Approaches
Accuracy comparisons
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 49: Hybrid Performance Estimation Approaches
Speedup comparisons
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 50: Hybrid Performance Estimation Approaches
Kim et al. [CODES+ISSS 2003] proposed another hybrid performance estimation approach
  static performance-estimation technique based on a queuing analysis as the first step to prune the design space
  simulation-based approach to accurately explore the reduced design space as the second step
  Limitations
    static queuing approach insufficient to handle complex bus protocol features (e.g., SPLIT/OO transactions, OO transaction completion)
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 51: Summary
Static performance estimation techniques
  + enable fast, early performance estimation
  - unable to account for dynamic effects that can have a significant effect on performance
Dynamic performance estimation techniques
  + provide accurate and reliable performance results,
  - can become time consuming for large applications
Hybrid performance estimation techniques
  combine static and dynamic performance estimation strategies
  can speed up communication architecture performance estimation while generating accurate performance exploration results
© 2008 Sudeep Pasricha & Nikil Dutt
<number>

## Slide 52
<number>
© 2008 Sudeep Pasricha & Nikil Dutt