## Slide 1: On-Chip Communication Architectures
Emerging On-Chip
Interconnect
Technologies
ICS 295
Sudeep Pasricha and Nikil Dutt
Slides based on book chapter 13
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 2: Outline
Introduction
Optical Interconnects
RF/Wireless Interconnects
CNT Interconnects
Conclusion
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 3: Introduction
Modern on-chip electrical interconnects (EIs) are realized using copper wires
On-chip EIs can be classified into two categories
  local interconnects: used for short distance communication and have a delay of less than a clock cycle
  global interconnects: which are fewer in number, used for long distance communication and have a delay spanning multiple cycles
Long global EIs typically have high RC constants
  which results in greater propagation delay, transition time, and crosstalk noise
Repeater insertion and increasing wire width can reduce the propagation delay somewhat
  delay is still quite large in DSM technologies
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 4: Introduction
In DSM technologies, it is becoming increasingly harder for a copper-based electrical interconnect (EI) to satisfy design requirements
  delay, power, bandwidth, delay uncertainty
Resistance of copper interconnects, in current and imminent technologies is increasing rapidly due to
  enhanced grain boundary scattering
  surface scattering
  presence of a highly resistive diffusion barrier layer
Steep rise in parasitic resistance and capacitance of copper interconnects poses serious challenges for
  interconnect delay (especially at the global level)
  power dissipation
  interconnect reliability
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 5: Introduction
Copper interconnects also constitute up to 70% of total on-chip capacitance
  major sources of power dissipation
According to the International Technology Roadmap for Semiconductors (ITRS), interconnect innovation with new technologies is vital
  to satisfy performance, reliability, power requirements in long term
  support ultra-high data rates (greater than 100 Gbps/pin)
  be scalable enough to support tens to hundreds of concurrent communication streams
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 6: Outline
Introduction
Optical Interconnects
RF/Wireless Interconnects
CNT Interconnects
Conclusion
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 7: Optical Interconnects
Optical interconnects (OIs) have potential to overcome communication bottleneck by replacing electrical wires with optical waveguides
OIs offer many advantages over traditional electrical (copper-based) interconnects
  can support enormous intrinsic data bandwidths in the order of several Gbps using only simple on–off modulation schemes
  relatively immune to electrical interference due to crosstalk, and parasitic capacitances and inductances
  power dissipation is completely independent of transmission distance at the chip level
  routing and placement is simplified since it is possible to physically intersect light beams with minimal crosstalk.
  once a path is acquired, transmission latency of the optical data is very small, depending only on the group velocity of light in the waveguide
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 8: Optical Interconnects
While board-to-board and chip-to-chip OIs have been proposed and are actively under development, feasibility of on-chip OIs is an open research problem
High speed, electrically driven, on-chip monolithic light source still remains to be realized
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 9: Optical Interconnects
(Off-chip) laser source
  provides light to modulator
Transmitter
  electro-optical modulator
    transduces electrical data supplied from electrical driver into a modulated optical signal
    several high speed electro-optical modulators have been proposed
      that change refractive index or absorption coefficient of an optical path when an electrical signal is injected
    Mach-Zehnder interferometer-based silicon modulators
      higher modulation speeds (several GHz)
      large power consumption
      greater silicon footprint (around 10 mm)
    Microresonator-based P-I-N diode type modulators
      compact in size (10–30 mm)
      low power consumption
      low modulation speeds (several MHz)
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 10: Optical Interconnects
Transmitter
  modulator driver
    consists of a series of inverter stages that drive the modulator ’s capacitive load
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 11: Optical Interconnects
Waveguide
  path through which light is routed
  refractive index of waveguide material has a significant impact on bandwidth, latency, and area of an OI
  two promising alternatives for waveguide material that trade-off propagation speed and bandwidth
    Silicon (Si)
      lower propagation speed, but low area footprint (higher bandwidth density)
    Polymer
      higher propagation speed but greater area (reduced bandwidth density)
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 12: Optical Interconnects
Receiver
  responsible for converting the optical signal back to an electrical signal
  photo-detector
    must have high value for quantum efficiency
      lower losses when converting optical information into an electrical form
    e.g. interdigitated metal–semiconductor–metal (MSM) receivers
      fast response and excellent quantum efficiency
  wave selective filter
    optional – only used when(WDM) is used
    selects among different wavelengths
  trans-impedance amplifier (TIA) stage
    converts photo-detector current to a voltage which is thresholded by subsequent stages to digital levels
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 13: Optical Interconnects
OIs possess an intrinsic advantage of low signal propagation delay in waveguides
  due to the absence of RLC impedances
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 14: Optical Interconnects
OIs require an electrical signal to be first converted into an optical signal and then back into an electrical signal
  conversion delay independent of interconnect length
OIs will have a delay advantage over EIs only if waveguide propagation delay dominates overall delay
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 15: Optical Interconnects
Minimum pitch between two adjacent waveguides is determined by crosstalk considerations
  for a fixed pitch, if waveguide is too wide, then crosstalk is high due to proximity between sides of adjacent waveguides
  If waveguide is too narrow, optical mode becomes less confined, causing a higher crosstalk due to larger overlap between adjacent optical modes
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 16: Optical Interconnects
Trade-off between waveguide density and propagation delay per unit length for a 10 mm interconnect and a maximum allowed crosstalk of 20%
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 17: Optical Interconnects
Comparison of projected bandwidth density for delay-optimize EIs and optical waveguides
  optical bandwidth density increases due solely to the higher bit rate through waveguides with a fixed pitch
  EIs exploit more efficient repeaters – leads to higher growth in bandwidth density
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 18: Optical Interconnects
Single wavelength OI is inferior to a delay-optimized EI in terms of bandwidth density
Why would anyone use OIs?
Wavelength division multiplexing (WDM) can improve bandwidth density for OIs over EIs
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 19: Optical Interconnects: Research
A few research efforts have studied how on-chip optical networks can be used for clock-tree networks
  can reduce clock distribution skew on chip in multi-GHz range
Intel researchers have claimed that WDM can enable optics to achieve high bandwidth, low latency for global signaling
  but this requires efficient high speed, low capacitance CMOS-compatible modulators, detectors, and practical WDM schemes
Chen et al. [TED 2004] argued that there is no significant skew and power advantages in using an optical solution
  as most of skew, power of clk signaling arises in local clk distribution
Ackland et al. [CICC 2005] showed that an optical clock tree scales better than an H-tree electrical clock network
  best solution might be a hybrid tree network, with optical front end and backend with small electrical trees
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 20: Optical Interconnects: Research
A few recent works have proposed using optical links in an on-chip network-on-chip (ONoC)
  O’Connor [SLIP 2004] and Briere et al. [RSP 2005] gave a high level overview of a 4x4 2D mesh based optical NoC
  Shacham et al. [DAC 2007] described a 2-D folded torus optical NoC
    can theoretically result in high bandwidth, low power intra-chip comm.
  Kirman et al. [MICRO 2006] proposed an optical loop network
    Si waveguide on dedicated layer
    support for WDM to improve bandwidth density
However ONoCs have a few drawbacks
  high power overhead of electrical routers and opto-electric/electro-optic conversion at the interface of each component
  lack of availability of wideband photonic switching elements
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 21: Optical Interconnects: Research
Recently, Pasricha et al. [ASPDAC 2008] proposed the ORB (optical ring bus) on-chip communication architecture
  novel opto-electric communication architecture that uses an ORB as a global interconnect between computation clusters
  preserves standard protocol interface (e.g., AMBA AXI) for inter- and intra-cluster communication
  hybrid Mach-Zehnder interferometer/microresonator-based P-I-N diode modulators
  ring-shaped low refractive index polymer waveguide
  support for WDM
  shown to dissipate significantly lower power (more than a 10x less) and improve overall performance (more than 2x)
    compared to traditional pipelined, all-electrical global interconnects, across the 65–22 nm CMOS technology nodes
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 22: Optical Interconnects: Open Problems
Efficient transmitter and receiver components
  high speed, low power, and small feature-size electro-optical modulators and photo-detector receivers need to be developed
Integrated on-chip light source
  such as the Indium Phosphide Hybrid Silicon Laser from Intel and UCSB [2008]
Polymer waveguide
  prohibitive manufacturing cost and complexity
  require suitable modulators
Temperature management
  OIs sensitive to temperature variations
  active or passive optical control method required to maintain stable device operation
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 23: Outline
Introduction
Optical Interconnects
RF/Wireless Interconnects
CNT Interconnects
Conclusion
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 24: RF/Wireless Interconnects
Replace on-chip wires with integrated on-chip antennas communicating via electromagnetic waves
Data is converted from baseband (i.e., digital) to RF/microwave signals and transmitted through free space or guided mediums
Free space signal broadcasting and reception is a common practice in modern wireless systems
  due to low cost implementation and excellent channeling capabilities
However, free space transmission and reception of RF/microwave signals requires an antenna size that is comparable to its wavelength
  even at near 100 GHz operating and cut-off frequencies in the future the aperture size of the antenna = 1 mm2 which is too large
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 25: RF/Wireless Interconnects
Microwave transmission in guided mediums such as microstrip transmission line (MTL) or coplanar waveguide (CPW) is a more viable alternative to free space
  low attenuation up to at least 200 GHz
  requires a smaller antenna size
Simulation results have shown that a 1cm long CPW experiences extremely low loss (1.6 dB at 100 GHz), and low dispersion (less than 2 dB for 50–150 GHz)
  EIs have 60 and 115 dB loss per cm at 100 GHz, and a freq dispersion of 30–40 dB
Thus microwave transmission over MTL or CPW has a clear advantage over conventional EIs
  especially for global interconnects operating in multi-GHz range
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 26: RF/Wireless Interconnects
RF/wireless interconnect
  multiple transmitters receivers
  capacitive couplers as near-field antennas
  RF circuits for transceivers
  uniform and homogeneous MTL or CPW channel as a shared bidirectional broadcasting medium
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 27: RF/Wireless Interconnects
Simultaneous communications in RF/wireless interconnects possible using frequency division multiple access (FDMA)
  RF modulated frequency bands can improve data bandwidth by transmitting data over multiple frequency bands
  frequency bands of I/O channels can be allocated between 5–105 GHz with a bandwidth of approximately 5–40 Gbps in each channel
    EIs only occupy lowest frequency band (baseband)
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 28: RF/Wireless Interconnects
Balanced or double balanced active mixers, such as the Gilbert cell, may be used for modulation and demodulation
Low loss and high selective BPFs needed in FDMA interconnects require tunable and high Q inductors
  which are hard to realize due to their high energy loss to the conductive silicon substrate
  can be partially resolved by using a transformer type inductor design
    where lost energy is recovered via a secondary inductor with delayed phase angles to attain high inductance and tunability
Recent progress in MEMS (microelectromechanical systems) has shown promise for high Q silicon resonators and filters
  in micrometer wave frequencies
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 29: RF/Wireless Interconnects
Simultaneous communications in RF/wireless interconnects possible using code division multiple access (CDMA)
  data stream from a transmitter is first converted into a spread spectrum signal by orthogonal Walsh codes (or PN codes)
  subsequently modulated with RF sinusoidal carrier
  resulting signal from transmitters are capacitively coupled into a superposed multilevel signal on the shared CPW (or MTL)
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 30: RF/Wireless Interconnects
Unlike hardware-oriented FDMA interconnect, the CDMA interconnect can be easily reconfigured by changing spreading codes through software commands
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 31: RF/Wireless Interconnects
On-chip antennas fabricated on substrates are categorized as printed antennas
  microstrip, dipole, and loop antennas
  linear meander
  zig-zag folded
Combining different antenna structures such as folded and meander can provide a higher power gain and a more compact on-chip antenna structure
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 32: RF/Wireless Interconnects
Some recent research has focused on using on-chip silicon substrate/dielectric layer as a transmission path
  instead of using off-chip and in-package CPW or MTL guided mediums
At 24 GHz, wavelength of EM waves in silicon is 3.7 mm
  a quarter wave antenna needs to be only about 0.9 mm in silicon
  in conjunction with increased chip sizes of 2 cm x 2 cm, has made the integration of antennas for wireless on-chip communication feasible
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 33: RF/Wireless Interconnects
Paths formed by
  passage through air
  refraction through the SiO2 layer and reflection at the interface between the silicon substrate and the underlying dielectric layer (A1N)
  refraction through the SiO2 and dielectric layers, and reflection by the metal chuck that emulates a heat sink in the back of a die
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 34: RF/Wireless Interconnects
Signals propagating on these multiple paths constructively and destructively interfere
It was found by O et al. [ICCAD 2005] that by increasing the AIN thickness, destructive signal interference is significantly reduced
Benech et al. [IECON 2006] conducted a similar feasibility study and found that
  higher resistivity substrates are better suited for wireless communication
  showed that antennas on lower resistivity silicon substrate present gains of 30 dB
  in contrast, antennas on SOI (silicon on insulator) substrates of higher resistivity present gains of 15 dB
    at frequencies around 30 GHz
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 35: RF/Wireless Interconnects: Research
Wireless interconnects may not only reduce the wires in integrated circuits, but can also be used to replace I/O pins
O et al. [GMAC 1999] proposed RF/wireless interconnects for clock networks to reduce signal skew
Test chips have been created to demonstrate the feasibility of RF/wireless on-chip interconnects and their use in clock networks
  Guo et al. [SVLSI 2002] showed that a 15 GHz transmitted signal 2.2 cm away from a clock receiver with an on-chip antenna was successfully picked up by receiver and used to generate digital output
  Floyd et al. [ISSCC 2000] presented another wireless clock implementation at 7.4 GHz frequency
    Transmitting and receiving antenna placed 3.3 mm from each other
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 36: RF/Wireless Interconnects: Open Problems
Packaging and interference issues
  metal structures near antennas can change input impedances and phase of received signals
  interference effects between the transmitted/received signal and switching noise of nearby circuits
Ultra-high frequency requirements
  for antenna sizes to be feasible for on-chip fabrication, RF circuits must operate in the ultra-high frequency domain (i.e., ~100 GHz range)
  unsuitable for applications in the very near future
  may be feasible by 2015 if scaling trends continue
Power overhead
  each transceiver has its own dedicated RF and CDR circuits
    heavy circuit overhead as well as large power consumption
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 37: RF/Wireless Interconnects: Open Problems
On-chip antennas
  lot of research on fabricating antennas on lossless or lower loss substrates such as polytetrafluoroethylene (PTFE), quartz, duroid, and GaAs in the millimeter wave range
  not been sufficient research in the area of fabricating printed antennas on silicon substrate
    much more lossy than other types of substrates
    reduces the antenna efficiency, requiring possibly greater power
Reference crystal oscillator
  required for FDMA
  cannot be easily implemented on-chip - has a large size
Security
  RF/wireless interconnects may be susceptible to hackers
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 38: Outline
Introduction
Optical Interconnects
RF/Wireless Interconnects
CNT Interconnects
Conclusion
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 39: CNT Interconnects
Carbon nanotubes are CNTs are sheets of graphite rolled into cylinders of diameters varying from 0.6 to about 3 nm
Demonstrate either metallic or semiconducting properties
  depending on direction in which they are rolled (chirality)
CNTs are promising candidates as on-chip interconnects
  high mechanical and thermal stability
  high thermal conductivity
  large current carrying capacity
  highly resistant to electromigration and other sources of breakdown
  much better conductivity properties than Cu
    due to longer electron mean free path (MFP) lengths in the micrometer range, compared to nanometer range MFP lengths for Cu
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 40: CNT Interconnects
It is predicted that isolated CNTs can replace Cu at the local interconnect level
  because of their much lower lateral capacitance which improves latency for very short distances
However, for longer on-chip interconnections a bundle of CNTs conducting current in parallel are more suitable
  because of high intrinsic resistance of an isolated CNT (> 6.45 KΩ)
A bundle of CNTs consists of
  metallic nanotubes that contribute to current conduction, and
  semiconducting nanotubes that do not contribute to current conduction in an interconnect
CNTs broadly classified into
  SWCNT: isolated (single walled) CNT
  MWCNT: multi-walled CNT, made up of concentric SWCNTS
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 41: Circuit Parameters for SWCNT
Resistance
  fundamental resistance RF = h/4e2 = 6.45kΩ for lengths less than MFP
    MFP (L0) is of electrons is distance across which no scattering occurs
    for SWCNTS, practical value of MFP is about 1µm
  for lengths less than L0, the resistance of a SWCNT is independent of length
  for lengths larger than L0, resistance increases with length, and this can be expressed as RSWCNT = RF . (L/L0)
  An additional source of resistance in SWCNTs is due to presence of imperfect metal-nanotube contacts
  total resistance for SWCNTs (sum of fundamental, scattering and contact) can be extremely high for longer interconnect lengths
    therefore isolated SWCNTs more suitable as local interconnects
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 42: Circuit Parameters for SWCNT
Capacitance
  electrostatic capacitance
    d = SWCNT diameter
    y = distance from ground plane
    y > 2d
  quantum capacitance
    h = Planck’s constant
    vF = Fermi velocity
    SWCNT has four conducting channels
    the effective quantum capacitance due to four parallel capacitances is 4CQ
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 43: Circuit Parameters for SWCNT
Inductance
  magnetic inductance
  kinetic inductance
    four parallel conducting channels in a CNT give rise to an effective kinetic inductance of LK/4
  typically, LK >> LM
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 44: Circuit Parameters for SWCNT Bundle
SWCNT bundles have lower resistance than SWCNTs
In a bundle, each SWCNT is surrounded by six immediate neighbors, with their centers separated by a distance x
  densely packed bundle with x = d is desirable
  in reality, not all SWCNTs of a bundle are metallic
    there are non-metallic SWCNTs that do not contribute to current conduction
    their presence is taken into account by considering a “sparsely” populated SWCNT bundle model, where x > d
  metallic density (Pm) of an SWCNT bundle refers to the probability that an SWCNT in the bundle is metallic (Pm ≈ 1/3 today)
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 45: Circuit Parameters for SWCNT Bundle
Resistance
Capacitance
  electrostatic capacitance arises mainly from SWCNTs lying at edges of bundle that are capacitively coupled with adjacent interconnects (left and right neighbors) as well as the substrate
Inductance
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 46: Comparison between Copper and SWCNT-Bundles
Resistance and capacitance of Cu and CNT bundle interconnects for local interconnect lengths
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 47: Comparison between Copper and SWCNT-Bundles
Propagation delay for local interconnects (dense bundle)
  delay for densely packed CNT bundles is higher than that with Cu interconnects across all technology generations
    even if contacts are perfect and an MFP as large as 10 µm is achieved
  higher capacitance of dense CNT bundles and high resistance of minimum sized drivers at the local interconnect level overshadow advantage from low CNT bundle resistance
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 48: Comparison between Copper and SWCNT-Bundles
Propagation delay for local interconnects (sparse bundle)
  performance of CNT bundles with perfect contacts becomes better than Cu wires if the distance between adjacent metallic CNTs forming a bundle is increased (i.e., sparser)
  however, with realistic (i.e., imperfect) contacts, delay is still higher than Cu interconnects
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 49: Comparison between Copper and SWCNT-Bundles
Propagation delay for local-intermediate length interconnects
  beyond a certain minimum length, performance of dense CNT bundle interconnects at this level is better than Cu wires
  with technology scaling, this minimum length decreases while the improvement in performance increases
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 50: Comparison between Copper and SWCNT-Bundles
Propagation delay for global interconnects
  global interconnects implemented with dense CNT bundles can achieve significantly better performance than copper
  however this performance improvement depends on CNT MFP
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 51: Multi-Wall Carbon Nanotubes (MWCNT)
MWCNTs may have diameters in a wide range varying from a few to hundreds of nanometers
  SWCNTs have diameters in the few nanometer range
MWCNT made up of SWCNTs with varying diameters
  have many of the properties of SWCNTs
  if properly connected to contacts, all MWCNT shells can conduct
Conductance of a SWCNT graphene shell in a MWCNT increases as the diameter of a shell becomes larger
Number of shells is given as
  δ = 0.34 is spacing between concentric shells
  ratio of Douter/Dinner has been observed to vary from 0.35 to 0.8
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 52: Multi-Wall Carbon Nanotubes (MWCNT)
Preliminary results indicate that for long lengths (hundreds of micrometers) MWCNTs can have conductivities several times larger than that of Cu or SWCNT bundles
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 53: Carbon Nanotube Interconnect: Open Problems
Inefficient metal-nanotube contacts
  makes propagation delay with CNT interconnects higher than with Cu interconnects
Small MFP length
  MFP lengths need to be increased to reduce CNT propagation delay
Density of nanotube bundles
  needed for global CNT interconnects that perform better than Cu interconnects
Inductive effects at high frequencies
  currently inductive effects are ignored but expected to become significant at very high frequencies
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 54: Summary
Traditional Cu interconnects have high resistivity, low reliability, and high susceptibility to electromigration
Novel on-chip interconnection schemes need to be explored for future high frequency electronic systems
Reviewed three of the most promising emerging interconnect technologies
  Optical interconnects
  RF/wireless interconnects
  Carbon nanotube interconnects
All of these technologies have several issues that must be resolved before they can be adopted as on-chip interconnect fabrics
  improvements in fabrication technology needed
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 55
<number>
© 2008 Sudeep Pasricha & Nikil Dutt