## Slide 1: On-Chip Communication Architectures
Standards
ICS 295
Sudeep Pasricha and Nikil Dutt
Slides based on book chapter 3
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 2: Outline
Why Standards?
On-chip standard bus architectures
  AMBA 2.0/3.0
  IBM CoreConnect
  STMicroelectronics’ STBus
  Sonics Smart Interconnect
Socket based on-chip bus interface standards
  OCP-IP
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 3: Why Standards?
SoC components (IPs) have an interface to the outside world consisting of a set of pins
  responsible for sending/receiving addresses, data, control
Number and functionality of pins must adhere to a specific interface standard
Important for seamless integration of SoC IPs – helps avoid integration mismatches
  e.g. 1 - connecting IP with 32 data pins to a 30 bit data bus
  e.g. 2 - connecting IP supporting data bursts to a bus with no burst support
Mismatches require development of “logic wrappers” at IP interfaces
  to ensure correct data transfers
  time consuming to create, reduce performance, take up area
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 4: Why Standards?
Interface standards define a specific data transfer protocol
  decide number and functionality of pins at IP interfaces
  make it easy to connect diverse IPs quickly
Two categories of standards for SoC communication:
  Standard bus architectures
    define interface between IPs and bus architecture
    define (at least some) specifics of bus architecture that implements data transfer protocol
  Socket based bus interface standards
    define interface between IPs and bus architecture
    freedom w.r.t choice and implementation of bus architecture
Ideally, designers want one standard to interconnect all IPs
In reality, several competing standards have emerged
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 5: Standard Bus Architectures
<number>
AMBA 2.0, 3.0 (ARM)
CoreConnect (IBM)
Sonics Smart Interconnect (Sonics)
STBus (STMicroelectronics)
Wishbone (Opencores)
Avalon (Altera)
PI Bus (OMI)
MARBLE (Univ. of Manchester)
CoreFrame (PalmChip)
…
widely used

## Slide 6: Standard Bus Architectures
<number>
AMBA 2.0, 3.0 (ARM)
CoreConnect (IBM)
Sonics Smart Interconnect (Sonics)
STBus (STMicroelectronics)
Wishbone (Opencores)
Avalon (Altera)
PI Bus (OMI)
MARBLE (Univ. of Manchester)
CoreFrame (PalmChip)
…

## Slide 7: AMBA 2.0
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 8: AHB Basic Transfer
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
Split ownership of Address and Data bus

## Slide 9: AHB Basic Transfer
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
Data transfer with slave wait states

## Slide 10: AHB Pipelining
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
Transaction pipelining increases bus bandwidth

## Slide 11: AHB Architecture
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
centralized arbitration / decode
1 unidirectional address bus (HADDR)
2 unidirectional data buses (HWDATA, HRDATA)
At any time only 1 active data bus

## Slide 12: AHB Arbitration
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
HBREQ_M1
HBREQ_M2
HBREQ_M3
Arbiter
Arbitration protocol is specified, but not the arbitration policy

## Slide 13: Cost of Arbitration in AHB
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
Time for arbitration
Time for handshaking

## Slide 14: AHB Pipelined Burst Transfers
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
Bursts cut down on arbitration, handshaking time, improving performance

## Slide 15: AHB Burst Types
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
Fixed length bursts
Incremental bursts access sequential locations
  e.g. 0x64, 0x68, 0x6C, 0x70 for INCR4, transferring 4 byte data
Wrapping bursts “wrap around” address if starting address is not aligned to total no. of bytes in transfer
  e.g. 0x64, 0x68, 0x6C, 0x60 for WRAP4, transferring 4 byte data

## Slide 16: AHB Control Signals
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
Transfer direction
  HWRITE – write transfer when high, read transfer when low
Transfer size
  HSIZE[2:0] indicates the size of the transfer

## Slide 17: AHB Control Signals
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
Protection control
  HPROT[3:0], provide additional information about a bus access

## Slide 18: AHB Split Transfers
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
Improves bus utilization
May cause deadlocks if not carefully implemented

## Slide 19: AHB Bus Matrix Topology
In addition to shared bus and hierarchical bus, AHB can be implemented as a bus matrix
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 20: APB State Diagram
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
When AHB wants
to drive a transfer
One cycle penalty for
APB peripheral address
decoding
Transfer occurs here
no (multi-cycle) bursts, pipelined transfers

## Slide 21: AHB-APB Bridge
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
AHB signals
High performance
Low power (and performance)

## Slide 22: AMBA 3.0
Introduces AXI high performance protocol
  Support for separate read address, write address, read data, write data, write response channels
  Out of order (OO) transaction completion
  Fixed mode burst support
    Useful for I/O peripherals
  Advanced system cache support
    Specify if transaction is cacheable/bufferable
    Specify attributes such as write-back/write-through
  Enhanced protection support
    Secure/non-secure transaction specification
  Exclusive access (for semaphore operations)
  Register slice support for high frequency operation
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 23: AHB vs. AXI Burst
AHB Burst
  Address and Data are locked together (single pipeline stage)
  HREADY controls intervals of address and data
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
AXI Burst
  One Address for entire burst

## Slide 24: AHB vs. AXI Burst
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
AXI Burst
  Simultaneous read, write transactions
  Better bus utilization

## Slide 25: AXI Out of Order Completion
With AHB
  If one slave is very slow, all data is held up
  SPLIT transactions provide very limited improvement
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
With AXI Burst
  Multiple outstanding addresses, out of order (OO) completion allowed
  Fast slaves may return data ahead of slow slaves

## Slide 26: Register Slices for Max Frequency
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
Register slices can be applied across any channel
Allows maximum frequency of operation by matching channel latency to channel delay
Allows system topology to be matched to performance requirements
WREADY
WID
WDATA
WSTRB
WLAST
WVALID

## Slide 27: Summary: AHB vs. AXI
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 28: Standard Bus Architectures
<number>
AMBA 2.0, 3.0 (ARM)
CoreConnect (IBM)
Sonics Smart Interconnect (Sonics)
STBus (STMicroelectronics)
Wishbone (Opencores)
Avalon (Altera)
PI Bus (OMI)
MARBLE (Univ. of Manchester)
CoreFrame (PalmChip)
…

## Slide 29: IBM CoreConnect
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
PLB
    Pipelined
    Burst modes
    Split transactions
    Multiple masters
OPB
    Low bandwidth
    Burst mode
    Multiple Masters
DCR
    Low throughput
      1 r/w = 2 cycles
    Ring type data bus

## Slide 30: Processor Local Bus (PLB)
High performance synchronous bus
  Shared address, separate read and write data buses
  Support for 32-bit address, 16, 32, 64, and 128-bit data bus widths
  Dynamic bus sizing—byte, half-word, word, and double-word transfers
  Up to 16 masters and any number of slaves
  AND–OR implementation structure
  Variable or fixed length (16-64 byte) burst transfers
  Pipelined transfers
  SPLIT transfer support
  Overlapped read and write transfers (up to 2 transfers per cycle)
  Centralized arbiter
  Locked transfer support for atomic accesses
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 31: PLB Transfer Phases
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
Address and data phases are decoupled

## Slide 32: Overlapped PLB Transfers
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
PLB allows address and data buses to have different masters at the same time

## Slide 33: PLB Arbiter
Bus Control Unit
  each master drives a 2-bit signal that encodes 4 priority levels
  in case of a tie, arbiter uses static or RR scheme
Timer
  pre-empts long burst masters
  ensures high priority requests served with low latency
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 34: On-chip Peripheral Bus (OPB)
Synchronous bus to connect low performance peripherals and reduce capacitive loading on PLB
  Shared address bus, multiple data buses
  Up to a 64-bit address bus width
  32- or 64-bit read, write data bus width support
  Support for multiple masters
  Bus parking (or locking) for reduced transfer latency
  Sequential address transfers (burst mode)
  Dynamic bus sizing—byte, half-word, word, double-word transfers
  MUX-based (or AND–OR) structural implementation.
  Single cycle data transfer between OPB masters and slaves.
  Timeout capability to guarantee low latency for high priority xfers
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 35: Device Control Register (DCR) Bus
Low speed synchronous bus, used for on-chip device configuration purposes
  meant to off-load the PLB from lower performance status and control read and write transfers
  10-bit, up to 32-bit address bus
  32-bit read and write data buses
  4-cycle minimum read or write transfers
  Slave bus timeout inhibit capability
  Multi-master arbitration
  Privileged and non-privileged transfers
  Daisy-chain (serial) or distributed-OR (parallel) bus topologies
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 36: Standard Bus Architectures
<number>
AMBA 2.0, 3.0 (ARM)
CoreConnect (IBM)
Sonics Smart Interconnect (Sonics)
STBus (STMicroelectronics)
Wishbone (Opencores)
Avalon (Altera)
PI Bus (OMI)
MARBLE (Univ. of Manchester)
CoreFrame (PalmChip)
…

## Slide 37: Sonics Smart Interconnect
Consists of 3 synchronous bus-based interconnect specifications
  SonicsMX
    high performance interconnect fabric
  SonicsLX
    high performance interconnect fabric, but with less advanced features
  Synapse 3220
    peripheral interconnect designed to connect slower peripheral components
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 38: SonicsMX
High performance synchronous bus fabric
  Pipelined, non-blocking, multi-threaded communication support
  Split/outstanding transactions for high performance
  Configurable data bus width: 32, 64, or 128 bits
  Socket-based connection support, using native OCP 2.0 interface
  Bandwidth and latency-based arbitration schemes to obtain desired quality of service (QoS) for threads
  Register points (RPs) for pipelining long interconnects and providing timing isolation
  Protection mode support
  Advanced error handling support
  Fine-grained power management support
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 39: SonicsMX Topology
SonicsMX supports full crossbar, partial crossbar, and shared bus topology
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 40: SonicsMX Arbitration
Weighted QoS
  available bandwidth distributed among masters based on ratio of bandwidth weights configured for each master
Priority QoS
  extends bandwidth-based scheme above
    1-2 threads are assigned a static priority (guaranteed service)
    Other threads assigned bandwidth weights (best effort)
Controlled QoS
  dynamically switches between three arbitration schemes based on traffic characteristics
    Static priority (guaranteed service)
    Bandwidth weighted scheme (best-effort)
    Guaranteed Bandwidth allocation (guaranteed service)
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 41: SonicsLX
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
High performance synchronous bus fabric
  subset of SonicsMX feature set
  pipelined, multithreaded, non-blocking communication support
  weighted and priority QoS modes
  SPLIT transactions

## Slide 42: Synapse 3220
Synchronous bus targeted at low bandwidth, physically dispersed peripheral slave cores
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 43: Synapse 3220 Features
Up to 4 masters and 63 slaves
Up to 24-bit configurable address bus
Configurable data bus widths—8, 16, 32 bits
Fair arbitration scheme, with high priority allowed for a single initiator thread
Power management interface
Exclusive (semaphore) access support
Error detection and recovery—watchdog timer to identify unresponsive peripherals
Protection mode support
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 44: Standard Bus Architectures
<number>
AMBA 2.0, 3.0 (ARM)
CoreConnect (IBM)
Sonics Smart Interconnect (Sonics)
STBus (STMicroelectronics)
Wishbone (Opencores)
Avalon (Altera)
PI Bus (OMI)
MARBLE (Univ. of Manchester)
CoreFrame (PalmChip)
…

## Slide 45: STBus
Consists of 3 synchronous bus-based interconnect specifications
  Type 1
    Simplest protocol meant for peripheral access
  Type 2
    More complex protocol
    Pipelined, SPLIT transactions
  Type 3
    Most advanced protocol
    OO transactions, transaction labeling/hints
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 46: Type 1
Simple handshake mechanism
32-bit address bus
Data bus sizes of 8, 16, 32, 64 bits
Similar to IBM CoreConnect DCR bus
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 47: Type 2
Supports all Type 1 functionality
Pipelined transfers
SPLIT transactions
Data bus sizes up to 256 bits
Compound operations
  READMODWRITE
    Returns read data and locks slave till same master writes to location
  SWAP
    Exchanges data value between master and slave
  FLUSH/PURGE
    Ensure coherence between local and main memory
  USER
    Reserved for user defined operations
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 48: Type 3
Supports all Type 2 functionality
OO transaction completion
Requires only single response/ACK for multiple data transfers (burst mode)
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 49: STBus
All types have
  MUX-based implementation
  Shared, partial or full crossbar implementation
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 50: STBus Arbitration
Static priority
  Non-preemptive
Programmable priority
Latency based
  Each master has register with max. allowed latency (in clock cycles)
    If value is 0, master must be granted bus access as soon as it requests it
  Each master also has counter loaded with max. latency value when master makes request
  Master counters are decremented at every subsequent cycle
  Arbiter grants access to master with lowest counter value
  In case of a tie, static priority is used
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 51: STBus Arbitration
Bandwidth based
  Similar to TDMA/RR scheme
STB
  Hybrid of latency based and programmable priority schemes
  In normal mode, programmable priority scheme is used
  Masters have max. latency registers, counters (latency based scheme)
  Each master also has an additional latency-counter-enable bit
  If this bit is set, and counter value is 0, master is in “panic state”
  If one or more masters in panic state, programmable priority scheme is overridden, and panic state masters granted access
Message based
  Pre-emptive static priority scheme
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 52: Socket-based Interface Standards
Defines the interface of components
  Does not define bus architecture implementation
  Shield IP designer from knowledge of interconnection system, and enable same IP to be ported across different systems
  Requires Adaptor components to interface with implementation
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 53: Socket-based Interface Standards
Must be generic, comprehensive, and configurable
  to capture basic functionality and advanced features of a wide array of bus architecture implementations
Adaptor (or translational) logic component
  Must be created only once for each implementation (e.g. AMBA)
  – adds area, performance penalties, more design time
  + enhances reuse, speeds up design time across many designs
Commonly used socket-based interface standards
  Open Core Protocol (OCP) ver 2.0
    Most popular – used in Sonics Smart Interconnect
  VSIA Virtual Component Interface (VCI)
    Subset of OCP
  DTL
    Proprietary
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 54: OCP 2.0
Point-to-point synchronous interface
Bus architecture independent
Configurable data flow (address, data, control) signals for area-efficient implementation
Configurable sideband signals to support additional communication requirements
Pipelined transfer support
Burst transfer support
OO transaction completion support
Multiple threads
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 55: OCP 2.0 Signals
Dataflow
  Basic signals
  Simple extensions
    e.g. byte enables, data byte parity, error correction codes, etc.
  Burst extensions
    e.g. length, type (WRAP/INCR), pack/unpack, ACK requirements etc.
  Tag extensions
    Assign IDs to transactions for reordering support
  Thread extensions
    Assign IDs to threads for multi-threading support
Sideband (optional)
  Not part of the dataflow process
  Convey control and status information such as reset, interrupt, error, and core-specific flags
Test (optional)
  add support for scan, clock control, and IEEE 1149.1 (JTAG)
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 56: OCP 2.0 Protocol Hierarchy
Data flow signals combined into groups of request signals, response signals and data handshake signals
Groups map one-on-one to their corresponding protocol phases (request, response, handshaking)
Different combinations of protocol phases are used by different types of transfers (e.g. ‘single request/multiple data burst’)
Burst transactions are comprised of a set of transfers linked together having a defined address sequence and no. of transfers
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 57: OCP 2.0 Profiles
OCP 2.0 specifies pre-defined configurations of interface called “profiles”
  consist of OCP interface signals, specific protocol features, and application guidelines
Two sets of profiles are provided
  Profiles for new IP cores implementing native OCP interfaces
    Block data flow
    Sequential undefined length data flow (streaming access)
    Register access
  Profiles for designers of bridges between OCP & other bus protocols
    Simple H-bus
    X-bus packet write
    X-bus packet read
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 58: Example: SoC with Mixed Profiles
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 59: Summary
Standards important for seamless integration of SoC IPs
  avoid costly integration mismatches
Two categories of standards for SoC communication:
  Standard bus architectures
    define interface between IPs and bus architecture
    define (at least some) specifics of bus architecture that implements data transfer protocol
    e.g. AMBA 2.0/3.0, Coreconnect, Sonics Smart Interconnect, STBus
  Socket based bus interface standards
    define interface between IPs and bus architecture
    do not define bus architecture implementation specifics
    e.g. OCP 2.0
Open Issue: Robust standards for DSM-aware communication
© 2008 Sudeep Pasricha & Nikil Dutt
<number>