## Slide 1: On-Chip Communication Architectures
Introduction
ICS 295
Sudeep Pasricha and Nikil Dutt
Slides based on book chapters 1, 2
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 2: Outline
Introduction to SoC Design Trends
Significance of on-chip communication architectures
Bus-based communication architectures
  Terminology
  Physical structure
  Clocking
  Arbitration and decoding
  Topology types
  Data transfer modes
  Physical implementation issues
  DSM effects
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 3: Designer Productivity Gap
© 2008 Sudeep Pasricha & Nikil Dutt
<number>
SoC designs today are complex, characterized by more and more IPs being integrated on a single chip, and a shrinking time-to-market

## Slide 4: Emerging Application Requirements
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 5: Coping with SoC Complexity
© 2008 Sudeep Pasricha & Nikil Dutt
<number>
Practicing IP based Design and Reuse
  Raising the reuse factor from standard cells to IP blocks
    e.g. predesigned hardware IPs for processors (ARM, PowerPC), communication (AMBA, CoreConnect), memories (Samsung SDRAMs, Denali SRAMs), I/O (UART, USB) etc.
  IPs not just for hardware, but for software (device drivers, OS) too
  Substantial reduction in SoC design and verification time
  Requires initial investment to create reusable cores
    but productivity improves with reuse
IP Interfacing Standards
  IP based design needs to handle incompatible IP interfaces
  Assembling heterogeneous IPs for SoC design can take months!!!
  Need for unified standard to quickly connect IPs
    e.g. OCP-IP, VSIA VCI etc.

## Slide 6: Coping with SoC Complexity
© 2008 Sudeep Pasricha & Nikil Dutt
<number>
Platform based Design
  Design paradigm which promotes IP based design and reuse
  A meet-in-the-middle approach
    maps application to a customizable design consisting of HW, SW IPs
  Platforms use IPs; but will soon become the IPs of the future
    e.g. Phillips Nexperia, ARM PrimeXsys platform etc.
Decouples the application development process from the architectural implementation process.

## Slide 7: Data Flow Replacing Data Processing As Major SoC Design Challenge
© 2008 Sudeep Pasricha & Nikil Dutt
<number>
I/O Bus
Main Bus
Core N
µP
Core 2
µP
Sub system
µP
Mem Bus
Core 1
SoCs
Circa 2002
SoCs Circa 2008
Critical Decision Was uP Choice
Critical Decision Is Interconnect Choice
Communication Architecture Design and Verification becoming Highest Priority in Contemporary SoC Design!
DRAMC
Exploding core counts requiring more advanced Interconnects
EDA cannot solve this architectural problem easily
Complexity too high to hand craft (and verify!)
Source: SONICS Inc.

## Slide 8: Examples of On-chip Communication Architectures
IBM Cell ring bus communication architecture
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 9: Ideal ESL Design Flow
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 10: Need for Communication-centric Design Flow
Communication is THE most critical aspect affecting system performance
Communication architecture consumes upto 50% of total on-chip power
Ever increasing number of wires, repeaters, bus components (arbiters, bridges, decoders etc.) increases system cost
Communication architecture design, customization, exploration, verification and implementation takes up the largest chunk of a design cycle
Communication Architectures in today’s complex systems significantly affect performance, power, cost and time-to-market!
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 11: Technology Scaling Trends: Total Interconnect Length on a Chip
Highlights importance of interconnect design in future technologies
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 12: Technology Scaling Trends: Interconnect Performance
Relative delay comparison of wires vs. process technology
Increasing wire delay limits achievable performance
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 13: Bus based On-Chip Communication Architectures
© 2008 Sudeep Pasricha & Nikil Dutt
<number>
Buses are the simplest and most widely used SoC interconnection networks
Bus:
  a collection of signals (wires) to which one or more IP components (which need to communicate data with each other) are connected
Only one IP component can transfer data on the shared bus at any given time
Micro-
controller
Digital
Signal
Processor
Input/
Output
Device
Memory
Bus

## Slide 14: Bus Terminology
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 15: Bus Terminology
© 2008 Sudeep Pasricha & Nikil Dutt
<number>
Master (or Initiator)
  IP component that initiates a read or write data transfer
Slave (or Target)
  IP component that does not initiate transfers and only responds to incoming transfer requests
Arbiter
  Controls access to the shared bus
  Uses arbitration scheme to select master to grant access to bus
Decoder
  Determines which component a transfer is intended for
Bridge
  Connects two busses
  Acts as slave on one side and master on the other

## Slide 16: Bus signal lines
© 2008 Sudeep Pasricha & Nikil Dutt
<number>
A bus typically consists of three types of signal lines
  Address
    Carry address of destination for which transfer is initiated
    Can be shared or separate for read, write data
  Data
    Carry information between source and destination components
    Can be shared or separate for read, write data
    Choice of data width critical for application performance
  Control
    Requests and acknowledgements
    Specify more information about type of data transfer
      Byte enable, burst size, cacheable/bufferable, write-back/through, …
address lines
data lines
control lines

## Slide 17: Types of Bus Topologies
Shared bus
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 18: Types of Bus Topologies
Hierarchical shared bus
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
Improves system throughput
  Multiple ongoing transfers on different buses

## Slide 19: Types of Bus Topologies
Split bus
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
Reduces impact of capacitance across two segments
Reduces contention and energy

## Slide 20: Types of Bus Topologies
Full crossbar/matrix bus (point to point)
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 21: Types of Bus Topologies
Partial crossbar/matrix bus
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 22: Types of Bus Topologies
Ring bus
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 23: Bus Physical Structure
tri-state buffer based bidirectional signals
Commonly used in off-chip/backplane buses
  + take up fewer wires, smaller area footprint
  - higher power consumption, higher delay, hard to debug
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 24: Bus Physical Structure
MUX based signals
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
Separate read, write channels

## Slide 25: Bus Physical Structure
AND-OR based signals
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 26: Bus Clocking
Synchronous Bus
  Includes a clock in control lines
  Fixed protocol for communication that is relative to clock
  Involves very little logic and can run very fast
  Require frequency converters across frequency domains
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 27: Bus Clocking
Asynchronous Bus
  Not clocked
  Requires a handshaking protocol
    performance not as good as that of synchronous bus
    No need for frequency converters, but does need extra lines
  Does not suffer from clock skew like the synchronous bus
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 28: Decoding and Arbitration
© 2008 Sudeep Pasricha & Nikil Dutt
<number>
Decoding
  determines the target for any transfer initiated by a master
Arbitration
  decides which master can use the shared bus if more than one master request bus access simultaneously
Decoding and Arbitration can either be
  centralized
  distributed

## Slide 29: Centralized Decoding and Arbitration
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
Minimal change is required if new components are added to the system

## Slide 30: Distributed Decoding and Arbitration
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
+ requires fewer signals compared to the centralized approach
- more hardware duplication, more logic/area, less scalable

## Slide 31: Arbitration Schemes
Random
  Randomly select master to grant bus access to
Static priority
  Masters assigned static priorities
  Higher priority master request always serviced first
  Can be pre-emptive (AMBA2) or non-preemptive (AMBA3)
  May lead to starvation of low priority masters
RR
  Masters allowed to access bus in a round-robin manner
  No starvation – every master guaranteed bus access
  Inefficient if masters have vastly different data injection rates
  High latency for critical data streams
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 32: Arbitration Schemes
TDMA
  Time division multiple access
  Assign slots to masters based on BW requirements
  If a master does not have anything to read/write during its time slots, leads to low performance
  Choice of time slot length and number critical
TDMA/RR
  Two-level scheme
  If master does not need to utilize its time slot, second level RR scheme grants access to another waiting master
  Better bus utilization
  Higher implementation cost for scheme (more logic, area)
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 33: Arbitration Schemes
Dynamic priority
  Dynamically vary priority of master during application execution
  Gives masters with higher injection rates a higher priority
  Requires additional logic to analyze traffic at runtime
  Adapts to changing data traffic profiles
  High implementation cost (several registers to track priorities and traffic profiles)
Programmable priority
  Simpler variant of dynamic priority scheme
  Programmable register in arbiter allows software to change priority
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 34: Bus Data Transfer Modes
Single Non-pipelined Transfer
  Simplest transfer mode
    first request for access to bus from arbiter
    on being granted access, set address and control signals
    Send/receive data in subsequent cycles
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 35: Bus Data Transfer Modes
Pipelined Transfer
  Overlap address and data phases
    Only works if separate address and data busses are present
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 36: Bus Data Transfer Modes
Non-pipelined Burst Transfer
  Send multiple data items, with only a single arbitration for entire transaction
    master must indicate to arbiter it intends to perform burst transfer
    Saves time spent requesting for arbitration
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 37: Bus Data Transfer Modes
Pipelined Burst Transfer
  Useful when separate address and data buses available
  Reduces data transfer latency
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 38: Bus Data Transfer Modes
Split Transfer
  If slaves take a long time to read/write data, it can prevent other masters from using the bus
  Split transfers improve performance by ‘splitting’ a transaction
    Master sends read request to slave
    Slave relinquishes control of bus as it prepares data
      Arbiter can grant bus access to another waiting master
      Allows utilizing otherwise idle cycles on the bus
    When slave is ready, it requests bus access from arbiter
    On being granted access, it sends data to master
  Explicit support for split transfers required from slaves and arbiters (additional signals, logic)
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 39: Bus Data Transfer Modes
Out-of-Order Transfer
  Allows multiple transfers from different masters, or even from the same master, to be SPLIT by a slave and be in progress simultaneously on a single bus
  Masters can initiate data transfers without waiting for earlier data transfers to complete
  Allows better parallelism, performance in buses
  Additional signals are needed to transmit IDs for every data transfer in the system
  Master interfaces need to be extended to handle data transfer IDs and be able to reorder received data
  Slave interfaces have out-of-order buffers for reads, writes, to keep track of pending transactions, plus logic for processing IDs
    Any application typically has a limited buffer size beyond which performance doesn’t increase
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 40: Bus Data Transfer Modes
Broadcast Transfer
  Every time a data item is transmitted over a bus, it is physically broadcast to every component on the bus
  Useful for snooping and cache coherence protocols
  Example: when several components on bus have a private cache fed from a single memory, a problem arises when the memory is updated
    when a cache line is written to memory by a component
  It is essential that private caches of the components on the bus invalidate (or update) their cache entries
    to prevent reading incorrect values
  Broadcasting allows address of the memory location (or cache line) being updated to be transmitted to all the components on the bus, so they can invalidate (or update) their local copies
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 41: Physical implementation issues for bus wires
Bus wires are implemented as long metal lines on a silicon wafer
  transmitting data using electromagnetic waves (finite speed limit)
As application performance requirements increase, clock frequencies are also increasing
  Greater bus clock frequency = shorter bus clock period
    100 MHz = 10 ns ; 500 MHz = 2 ns
Time allowed for a signal on a bus to travel from source to destination in a single bus clock cycle is decreasing
Can take multiple cycles to send a signal across a chip
  6-10 bus clock cycles @ 50 nm
  unpredictability in signal propagation time has serious consequences for performance and correct functioning of synchronous digital circuits
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 42: Physical implementation issues for bus wires
Partition long bus wires into shorter ones
  Hierarchical or split bus communication architectures
  Register slices or buffers to pipeline long bus wires
    enable signal to traverse a segment in a single clock cycle
Asynchronous buses
  No clock signal
Low level techniques
  Inserting repeaters or using fat wires
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 43: Buses in the DSM era
With CMOS process technology scaling below 90 nm, SoCs have entered the DSM era
  High levels of component integration
  High clock frequencies
  Low signal voltages
Buses significantly impacted by DSM effects
  Signal integrity issues
    scenario where the received signal at the destination is different from the transmitted signal at the source driver
    noise caused due to following factors
      crosstalk
      external electromagnetic interference
      transmission line effects
      soft errors
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 44: DSM Effects
Crosstalk
  Phenomenon of noise being caused on a signal A due to the coupling with another signal B
    due to the close proximity of bus wires
    near-field electromagnetic coupling causes inductive and capacitive crosstalk on bus signals
  Even when wires are far apart, crosstalk can still occur
    due to coupling facilitated by
      common substrate,
      shared power supply or ground, or
      a shared signal return path
  As wires become narrower with scaling and clock frequencies increase, fringing field effects and inductance effects become larger for wires
    higher inductive and capacitive crosstalk
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 45: DSM Effects
Electromagnetic interference (EMI)
  Phenomenon of large external electric and magnetic fields coupling into circuits and creating unwanted noise
  EMI due to external and internal coupling is expected to increase with evolving technology
    As highly integrated, portable wireless communication SoCs increasingly consist of analog, RF, and digital circuits
  Long on-chip buses in particular will be the sources and receptors of EMI noise
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 46: DSM Effects
Transmission line effects
  when a wire is longer than 1/10 of the wavelength of the signal frequency component that is transmitted, the wave nature of the propagated signal must be modeled
    otherwise significant errors may result.
  wires will thus have to be modeled as transmission lines to avoid errors during signal analysis
  Discontinuities in these transmission lines can result in impedence mismatches
    due to various factors such as capacitive loads, vias, wire bends, package pins, crossover wires, and non-ideal receivers
  Such mismatches will create noise as a result of signal reflections at the discontinuities
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 47: DSM Effects
Soft Errors
  Phenomenon of spurious pulses and interference with signals on buses
  Caused by
    collision of thermal neutrons
      produced by the decay of cosmic ray showers
    alpha particles
      produced by impurities in the substrate
  Highly integrated SoCs will be particularly susceptible to soft errors
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 48: DSM Effects
Harder to guarantee error-free data transfers on buses
Reduced signal swings in DSM technologies will result in a further reduction of voltage noise margins
  Greater probability of transmission errors in the presence of even the smallest sources of noise
Many other factors will further complicate bus design
  increasing wire resistance due to skin effect at high frequencies
  increasing number of metal layers that increase cross-layer coupling
  timing errors due to jitters
Emerging tools and methodologies for on-chip communication architecture design must predict and address DSM issues early in the design flow
  instead of finding and fixing the problems in post-layout
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 49: Summary
SoC complexity is increasing rapidly, due to
  Digital convergence
  Process technology shrinking into DSM era
On-chip communication architectures are critical components in SoC designs
  To meet power, performance, cost, reliability constraints
  Also rapidly increasing in complexity with increasing no. of cores
Reviewed basic concepts of (widely used) bus-based communication architectures
Open Problems
  Designing communication architectures to satisfy diverse and complex application constraints
  Predicting and estimating DSM issues early in a design flow
© 2008 Sudeep Pasricha & Nikil Dutt
<number>