## Slide 1: On-Chip Communication Architectures
Physical Design Trends
for Interconnects
ICS 295
Sudeep Pasricha and Nikil Dutt
Slides based on book chapter 11
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 2: Outline
Introduction
DSM Interconnect Design
Low Power High Speed Circuit Design Techniques
Power Distribution Techniques
Clock Distribution Techniques
3D Interconnects
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 3: Introduction
Smaller feature size in DSM technology nodes reduces delay of active devices
However, effect on delay due to the passive interconnects has increased rapidly
Local wire delay decreases with feature size due to a reduction in distance among active devices
However overall speed of current ICs is most often limited by the long distance global interconnects
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 4: Introduction
With shrinking feature size and larger chip die dimensions, sheer number of interconnects has increased exponentially
Interconnect capacitance often dominates total gate load
  therefore, a large portion of the total transient power is dissipated by these on-chip lines
  particularly true for those long interconnects that distribute the clock signals
    that can dissipate 40–50% of total IC power
Gains achieved in performance with technology scaling are often accompanied by an increase in power dissipation
  e.g., additional interconnect layers enhance circuit speed at the expense of higher power consumption due to the larger interconnect capacitance
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 5: Introduction
Traditionally used RC interconnect models are not sufficiently accurate to properly capture signal propagation in lines with fast transition times
Including inductance (L) in the RC model has become a necessary modification
  RLC models are therefore becoming increasingly common at the expense of greater computational cost
Whether to include inductance in the interconnect model at midrange frequencies (~ 1 - 3 GHz) depends on several factors
  e.g. the length of the line, cross-sectional area of the line, etc
Under certain conditions, ignoring line inductance may lead to high area and power inefficient circuits
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 6: Introduction
In addition to interconnects among the various on-chip devices, the clock and power distribution networks require significant metal resources
  both must span the entire chip
Accurately modeling the clock, power, and signal nets is a difficult task
  highly complex structures
Optimally allocating metal to properly design these networks presents an even greater challenge
  because of complexity in developing interconnect models
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 7: Outline
Introduction
DSM Interconnect Design
Low Power High Speed Circuit Design Techniques
Power Distribution Techniques
Clock Distribution Techniques
3D Interconnects
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 8: DSM Interconnect Design
Scaling of the lateral dimensions in planar devices, such as MOS transistors, has produced improvements in device
  area
  power
  speed
Power consumption and signal propagation delays of long (global) resistive lines have increased
Accurate on-chip interconnect models are required
  to determine the signal characteristics and design requirements of high speed DSM interconnect
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 9: DSM Interconnect Design
A local line can be modeled as a single lumped capacitor
  signal propagation delay is negligible compared to gate delay
Longer lines must include resistive effect
  Long interconnect models often divide the line into sections - distributed impedance model
    T or П
    accuracy depends on no. of sections
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 10: DSM Interconnect Design
Long, wide interconnects operating at frequencies exceeding a GHz are not accurately characterized by an RC model
  An RLC model is necessary for accuracy
  More complex to evaluate
  Distributed RLC model (T or П)
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 11: DSM Interconnect Design
  Length criteria for including inductance in interconnect model
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 12: DSM Interconnect Design
Frequency criteria for including inductance in interconnect models
  increasing signal frequencies require faster signal transition times
  resulting effect of a decreased signal transition time is a lower limit on the line length, making shorter on-chip interconnects behave inductively
    medium length lines can also behave inductively at high signal frequencies
  Dielectric material criteria for including inductance in interconnect models
  line capacitance can be reduced by half of the capacitance of SiO2 with the use of low k dielectrics
  copper interconnect has reduced the line resistance by a factor of two to three as compared to aluminum
  these and other new materials further the need to include line inductance in interconnect models
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 13: Outline
Introduction
DSM Interconnect Design
Low Power High Speed Circuit Design Techniques
Power Distribution Techniques
Clock Distribution Techniques
3D Interconnects
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 14: Low Power High Speed Circuit Design Techniques
High Speed Circuit Design Goal: Improve performance
Power and noise are important when considering design techniques to optimize circuit performance
Noise affects delay, degrades waveform shape, and most importantly, creates the possibility of an erroneous interpretation of the digital signals
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 15: CMOS Power Dissipation Overview
CMOS Power Dissipation
  Dynamic power
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 16: CMOS Power Dissipation Overview
  Short circuit power
    Due to current flow when a conductive path exists from the power rail to ground rail
  Leakage power
    Due to current that flows between the power terminals in the absence of any switching
    Increasingly dominating overall power
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 17: Wire Sizing
Width of an interconnect affects the power characteristics and propagation delay
Consider a CMOS inverter driving an RC interconnect line
  Simple first order model of delay
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 18: Wire Sizing
Increasing the driver transistor width reduces Rtr
  decreasing the circuit delay
  trading off circuit power and area for higher speed
Increasing the width of the interconnect to reduce Rint does not significantly reduce the delay caused by the RC interconnect impedance
  since decrease in wire resistance is offset by increase in wire capacitance
Many algorithms have been proposed to determine the optimum wire size that minimizes a target cost function
  minimizing delay
  addressing reliability issues by reducing clock skew
Few approaches for simultaneous driver and wire sizing
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 19: Wire Sizing
Tradeoffs exist between
dynamic and short-circuit
power
  As line inductance-to-resistance ratio increases with wider lines, short-circuit power decreases due to reduction in signal transition time
  For an RC line, short-circuit power remains approximately constant with increasing width (unlike RLC line shown in figure)
    decrease in interconnect resistance offset by an increase in capacitance
  If width of interconnect exceeds a specific limit, short-circuit power increases
    change in the matching characteristics between driver and interconnect
  Dynamic power increases with width since line capacitance is greater
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 20: Driver Sizing
Transistor sizing techniques aim to lower delay
Wider transistors have a few advantages but also several disadvantages
  + produce more current
  + reduce charge time of load capacitance
  – have greater physical area
  – have larger gate capacitance
  – increased circuit area and power
A careful balance of the current drive and output load is necessary to enhance circuit performance
Power optimal transistor size is smaller than the power-delay optimal transistor size
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 21: Tapered Buffers
An important example of transistor sizing is tapered buffers
  Used to drive large capacitive loads
Consists of chain of inverters of gradually increasing size
Ratio of size of an inverter to size of the preceding inverter is the tapering factor β
Delay of tapered buffer system is less than delay of a single large inverter
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 22: Tapered Buffers
Dependence of the tapered buffer propagation delay on tapering factor
<number>
© 2008 Sudeep Pasricha & Nikil Dutt
For minimum delay, optimal number of stages
  Nopt= ln(M)
  where M = CL/Co is the ratio of the load capacitance to the input capacitance of the initial inverter in the chain
Area, power, and delay strongly dependent on β
  Trade-offs possible by varying tapering factor

## Slide 23: Repeater Insertion
An effective strategy for reducing delay of a long interconnect is to strategically insert buffers along a line
Repeaters circumvent quadratic increase in interconnect delay by partitioning the line into smaller and approximately equal sections
Sum of section delays is smaller than delay of original path since delay of each section is reduced
Decreased interconnect delay is partially offset by the additional delay of the inserted repeaters
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 24: Repeater Insertion
Optimal number of repeaters
Optimal size of repeaters
Rt and Ct are the total interconnect resistance and capacitance
R0 and C0 are the input and output repeater resistance and capacitance
Cg0 is the input capacitance of the repeater
Fitting parameters a1 and a2 account for rise and fall time of the propagating signal
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 25: Repeater Insertion
For an RC line, repeater insertion techniques outperform wire sizing
In RLC lines, wire sizing outperforms repeater insertion as the minimum signal propagation delay with no repeaters is smaller
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 26: Outline
Introduction
DSM Interconnect Design
Low Power High Speed Circuit Design Techniques
Power Distribution Techniques
Clock Distribution Techniques
3D Interconnects
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 27: Power Distribution Techniques
Power grid consists of a supply, load, and interconnect lines connecting the supply to the load
Interconnect lines connecting the power supply to the load are non-ideal with a finite resistance and inductance,
  Rp , Lp and Rg , Lg , for the power and ground lines, respectively
Change in supply voltages at the load terminal is referred to as power supply noise
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 28: Power Distribution Techniques
Power supply noise can adversely affect circuit operation
Power supply variations reduce rail-to-rail power voltage, causing gate-to-source voltage across both NMOS and PMOS transistors to also decrease
  lowering the output drive current of these devices
  signal delay increases, compared to delay under nominal power supply voltage
Power noise affects propagating clock and data signals by causing an increase in both delay and delay uncertainty within the data paths
  severely limit the maximum operating frequency of an IC
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 29: Power Distribution Techniques
Power distribution network should exhibit a minimal impedance at terminals of the load
  to ensure a small variation in the power supply voltage
Decoupling capacitors ensure correct and reliable operation
  distributed across a system, placed at board, package, and on-chip levels
  provide charge when transient current demands on power grid are high
  each decoupling capacitor provides transient current to the load, effectively reducing the local transient noise
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 30: Power Distribution Techniques
On-chip current densities can reach several hundred thousand amperes per sq. cm, leading to electromigration
Electromigration is the transport of metal atoms under the force of an electron flux
  depletion and accumulation of metal material resulting from atomic flow can lead to formation of extrusions and voids in metal structures
  extrusions and voids can lead to short circuits and open circuit faults
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 31: Outline
Introduction
DSM Interconnect Design
Low Power High Speed Circuit Design Techniques
Power Distribution Techniques
Clock Distribution Techniques
3D Interconnects
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 32: Clock Distribution Techniques
In a synchronous digital system, the clock signal provides a time reference for movement of data within that system
Clock signals are typically
  loaded with the greatest fanout
  travel over the longest distances
  operate at the highest speeds of any signal, either control or data
Differences in the delay of the clock signals can
  severely limit the maximum performance of the entire system
  create catastrophic race conditions in which an incorrect data signal may latch within a register
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 33: Clock Distribution Techniques
Synchronous systems are composed of the following three delay components:
  memory storage elements
  logic elements
  clocking circuitry and distribution networks
Minimum allowable clock period TCP(min) between any two registers in a sequential data path is
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 34: Clock Distribution Techniques
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 35: Clock Distribution Techniques
Ideally, clocking events occur simultaneously at all registers
Difference in the clock signal arrival time between two sequentially adjacent registers is the clock skew
  system-wide or chip-wide clock skew between two non-sequentially adjacent registers, from an analysis viewpoint is meaningless
    has no effect on the performance and reliability of a synchronous system
  can be positive or negative
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 36: Clock Distribution Techniques
Under positive clock skew the maximum attainable operating frequency is decreased
  Performance degradation
Under negative clock skew maximum performance of a synchronous system can be improved by decreasing delay of a critical path
But there is also potential for a race condition
  clock skew must be less than the time required for
    data signal to leave initial register, propagate through interconnect and combinatorial logic, and successfully set up in the final register
  if this condition is not met
    data stored in register Rf is overwritten by data that had been stored in register Ri and has propagated through the combinatorial logic
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 37: Clock Distribution Techniques
The most common strategy for distributing on-chip clock signals is to insert buffers at the clock source and along the clock path, forming a tree structure
Buffers, acting as repeaters, are usually distributed throughout clock network
Distributed buffers serve the double function of
  amplifying clk signals degraded by distributed interconnect impedances
  isolating the local clock nets from the upstream load impedances
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 38: Clock Distribution Techniques
Another approach for distributing clock signals utilizes a hierarchy of planar symmetric H-tree or X-tree structures to ensure zero clock skew
  by maintaining identical distributed interconnect and buffer paths from clock signal source to the clocked registers
  conductor widths in H-tree structures are designed to progressively decrease as signal propagates to lower levels of the hierarchy
    ensuring that reflections are minimized at branch points
Drawbacks compared to standard clock trees:
  interconnect capacitance and power dissipation is much greater since total wire length is much longer
  difficult to implement in high complexity integrated systems which are typically irregular in nature
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 39: Outline
Introduction
DSM Interconnect Design
Low Power High Speed Circuit Design Techniques
Power Distribution Techniques
Clock Distribution Techniques
3D Interconnects
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 40: 3D Interconnects
3-D interconnects have been proposed as a way to address increasing line delay and capacitive crosstalk
Introduction of a third dimension significantly alters distribution of the interconnect length in ICs
  As the number of planes is increased, the length and number of the global (local) interconnects decrease (increase)
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 41: 3D Interconnects
It is possible to partition a 2-D IC into multiple subsections and stack these sections in the vertical dimension
  reduces corner-to-corner interconnect length significantly
  several global interconnects in the upper metallization levels can be transferred to local, smaller aspect ratio metal layers
    reduces the total number of metal levels within a 3-D circuit
  an increase in the clock frequency is possible as the worst case data path delay can be reduced
    assuming a constant number of registers along a sequential data path and number of metal layers
  consume less power as compared to 2-D ICs as a consequence of the reduced capacitive load of the global interconnect lines
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 42: 3D Interconnects
3-D interconnect system requires inter-plane interconnects that connect signals between vertically stacked devices
Inter-plane interconnects implemented as through silicon vias (TSV) or 3-D vias can produce the shortest path within a 3-D system
  as compared to wire bonding, peripheral vertical interconnects, and solder ball arrays
Much work is needed to properly characterize and model the interplane TSV
  primary technological innovation required to exploit benefits of 3-D integration
<number>
© 2008 Sudeep Pasricha & Nikil Dutt

## Slide 43: Summary
Complexity of properly designing interconnects in the DSM regime increases with each successive technology generation
  Choice between RC or RLC dependant on several factors
Low power, high speed circuit techniques are essential to expand battery lifetime and maintain ambient thermal levels
  Wire and driver sizing, as well as repeater insertion critical
Clock and power distribution are important applications of the general interconnect design problem
  noise and skew must be considered during design
Novel techniques such as 3D interconnects in interconnect design can help alleviate challenges in emerging ICs
  e.g. longer line lengths, greater line impedances, increased signal delays
© 2008 Sudeep Pasricha & Nikil Dutt
<number>

## Slide 44
<number>
© 2008 Sudeep Pasricha & Nikil Dutt